## Slide 1: Project Migration / Management

## Slide 2: Project Migration
Understand the Migration Path
  https://support.industry.siemens.com/cs/ww/en/view/62100731
Identify the components that make up the TIA Portal Engineering Software
Notes: Review the migration link to learn more about the restrictions and things to look out for when converting.

## Slide 3: Migration Path
S7-200 phased-out October 1, 2013
  Replaced by S7-1200
S7-300 & S7-400 after 2020
  Replaced by S7-1500
Notes: Major software development has stopped on Step 7 Classic.
Users should be planning for migration at this time.

## Slide 4: Compatibility
64Bit
32Bit
64Bit
32Bit
+ Windows Server 2012 R2
Classic
TIA Portal V14
Windows 7
Windows 8.1
Windows 10
+ Windows Server 2008 SP1
+ Windows Server 2008 R2 SP1

## Slide 5: Controller Portfolio
Advanced Controller
Distributed Controller
Basic Controller
  Unique power thanks to high performant backplane bus, shortest clamp-to-clamp reaction time and fastest signal processing
  Highest level of user-friendliness
  Space-saving distributed controller
  Combines the benefits of S7-1500 with the layout of ET 200SP.
  Compact controller, failsafe also!
  Modular expandable
  Wide range of integrated technology functions.
Software Controller
  PC-based controller for use on SIMATIC IPCs
  Runs independently: Restart of Windows while controller in run.
  PC-based controller for use on SIMATIC IPCs
  Runs independently: Restart of Windows while controller in run.
Notes: Advanced Controllers – what we normally consider when discussing PLCs
Software Controllers – referred to as soft controllers, are installed on PC har.dware. The user program is written and downloaded just like a traditional PLC.
Distributed Controllers – Lower end CPUs that attach directly to distributed IO. These are programmed like a traditional PLC.
Basic Controllers – Simple controllers with limited instruction set. Programmed like a traditional PLC but are the bridge between “relay replacer” PLCs (Siemens LOGO!) and other controllers.

## Slide 6: Controller Portfolio
ET 200SP modules
Basic Controller (S7-1200)
Advanced Controller (S7-1500)
Distributed Controller (ET 200SP CPU)
Software Controller S7-1500
CPU
Interface modules
Power supply
Communication modules
Signal modules
Technology modules
Switch modules
CPU
Power supply
Communication modules
Signal modules
Technology modules
Signal boards
CPU

## Slide 7: Standard S7-1500 CPU
412-2 PN/DP
414-3 PN/DP
412-1
412-2
1,000
2,000
3,000
4,000
6,000
315-2 DP
317-2 DP
317-2 PN/DP
312
314
315-2 PN/DP
319-3 PN/DP
414-3
414-2
416-2
7,000
5,000
S7-1500
1516
1513
1511
1515
1518
1517
German list price in €, regional adjustment may differ!
S7-1500 CPU Portfolio
7-3
7-3
CPU 1511-1 PN … CPU 1518-3 PN/DP

## Slide 8: Failsafe S7-1500 CPU
CPU 1511F-1 PN … CPU 1518F-3 PN/DP
414F-3 PN/DP
1,000
2,000
3,000
4,000
6,000
315F-2 DP
317F-2 DP
317F-2 PN/DP
315F-2 PN/DP
319F-3 PN/DP
416F-2
7,000
5,000
S7-1500
German list price in €, regional adjustment may differ!
1516F
1515F
1511F
1513F
1518F
1517F

## Slide 9: Compact S7-1500 CPU
500
1,000
1,500
312C
313C
S7-1500
SIMATIC CPU 1511C-1 PN / 1512C-1 PN
313C-2 PtP
313C-2 DP
314C-2 PtP
314C-2 DP
314C-2 PN/DP
Notes:
S7-300C incl. IO connector (Push-In)
CPU 313C has more IOs than CPU 1511C
1512C
1511C
German list price in €, regional adjustment may differ!

## Slide 10: Distributed Controllers ET200SP
CPU 1510SP-1 PN / CPU 1510SP F-1 PN CPU 1512SP-1 PN / CPU 1512SP F-1 PN

## Slide 11: TIA Portal Overview of the functional scope of the products
WinAC
S7-1200
S7-300 / S7-400
ET200 CPU
S7-1500
Professional
SIMATIC STEP 7
SIMATIC WinCC
SINAMICS Startdrive
Programming Languages
LAD, FBD, SCL, STL*, S7-Gragh*
Option STEP 7 Safety
Machine-level operator control and monitoring
SCADA applications
Drive configuration,
commissioning, diagnostics
SCADA
G120
PC Single User
G120D
Comfort Panels
G120P
Basic Panels
G120C
Communication
- Profibus, Profinet, network topology, (AS-I, IO-Link)
Shared functions
- System diagnostics, import/export to/from Excel, undo …..
Basic
Basic
Comfort
Advanced
Professional
Startdrive
*Only in Professional for S7-300/400/1500/WinAC
Notes: The TIA Portal is an engineering framework that combines PLC and HMI engineering into a single package. The three components of the TIA Portal are the PLC engineering software STEP7, the HMI engineering software WinCC, and the Drives engineering software Startdrive.
Step 7 – Engineering software for 1200, 1500 and WinAC. Additionally 300 and 400 can be programmed.
Basic – A master disk licensed product programs the 1200. LAD FBD SCL
Professional – several licenses are available for the different version and packages. Used to program 1200, 1500, WinAC, 300 and 400. Additionally STL and S7-Graph
WinCC – Engineering Software for all levels of HMI.
Basic – For use with Basic Panels. Master Disk License. License included with both Step7 License levels.
Comfort – Adds support for Comfort Panels
Advanced – Adds PC Runtime development
Professional – includes all other devices and full SCADA HMI solutions.
Startdrive – Engineering of Siemens drives. As of V13 G110, and G120 supported. S120 Planned for V14.

## Slide 12: Portal and Project View
Portal View
Project View
Notes: Switching between views can be done with the link in the lower left corner.
Switching permanently between views can be done;
Options  Settings  General  General  Start View

## Slide 13: Project View Objects
Project Tree
Details Window
Working Area
Inspector Window
Task Cards
Notes: Project Tree – Blocks, devices, traces and connectivity are found in the project tree
All other areas change based on what is selected on the screen.
Detail Window - Shows details regarding the selected item
Working Area – Area where hardware is assembled, code is written
Inspector Window – most parameterization is done is this area.
Task Cards – These are hardware libraries, instruction libraries and user developed faceplates, to name a few.
All windows can be floated, docked hidden, and minimized.

## Slide 14: Lab Exercises

## Slide 15: Lab1.1 – Migrate Classic Application
Notes: Extract the Classic Archive to the Desktop
Note the old file structure

## Slide 16
Notes: Open Portal
Click Project  Migrate Project
Find the classic application - *.s7p
Be sure to check to include hardware configuration
Click Migrate

## Slide 17: Lab1.2 – Archive and Retrieve
Notes: Archive the project
Click Project  Archive
Archives despite the file extension are simply windows zip files.
Close the project
Click Project  Close
Retrieve the project
Click Project  Retrieve

## Slide 18: Lab1.3 – Portal View / Project View
Notes: Note the difference between the Portal View and the Project view
Spend some time observing the differences.

## Slide 19: Lab 1.4 – Float and Dock Windows
Notes: Float the work window, auto hide the task cards, and Inspector Windows
Discover how the windows behave.